## Slide 1: ECE477 Midterm Design Review: Team #16
Abby Haluska
Team Lead
Cameron McCutcheon
Hardware Engineer
Joey Collins
Software Engineer
John Morton
Systems Engineer
Notes: - abby
-

## Slide 2: Outline
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions
Notes: - abby

## Slide 3: Project Overview
A robot designed to oppose a human player in a game of air hockey
  For hobbyists & enthusiasts
Uses computer vision to determine a puck’s trajectory
The microcontroller then adjusts the position of the paddle via motor control to defend and attack
Autonomous Air Hockey Robot
Notes: Abby
-
In this section provide a concise description of your project (you should start with your Project Description from your team website and then elaborate). What is it? What will it do? What differentiates it from similar projects and prior art? Include a relevant picture of your project or “artist rendering” of the completed project.

## Slide 4: PSDRs
PSDR #1 (Hardware): An ability to use a microcontroller to control the XY directions of a gantry system using PWM and 2 motors.
PSDR #2 (Hardware): An ability to interface with an IC to establish communication and send data between a microcontroller and a PC via UART.
PSDR #3 (Hardware): An ability to interface a seven-segment display scoreboard with shift registers.
PSDR #4 (Hardware): An ability to keep score with a microcontroller by counting the number of times an interrupt is triggered by a puck passing through an infrared laser beam.
PSDR #5 (Software): An ability to estimate the position and trajectory of a puck in motion using computer vision.
SPSDR #1 (Hardware): An ability to amplify a PWM signal using an amplifying circuit to produce sound using speakers in the scoreboard system.
SPSDR #2 (Hardware): An ability to use button input to determine robot reaction speed by adjusting motor speed in software.
Project Specific Design Requirements + Stretch Goals
Notes: Abby
- summarize PSDRs

## Slide 5: Major Components – micro
stm32f091rct6
Specifications:
# of I/O Pins
Clock speed
Independent communication channels
3.3V Operating Voltage
Options:
STM32F091RCT6
Teensy 3.0
ESP32 Wroom
Final Choice: STM32F091RCT6
ARM Cortex - familiar environment and community support
48 MHz max clock speed
Plenty of timers
Sufficient SPI + UART channels
Low cost
Notes: Abby
- esp32 was considered for wifi, ruled out once we decided uart
- teensy is costly, stm is $5
- stm has more uart and spi channels than teensy

## Slide 6: Major Components – Camera
ELP high speed Global Shutter camera
Specifications:
Framerate
Latency
Cost
Options:
ELP Camera
OptiTrack Flex 3
Raspberry Pi Camera Module
Final Choice: ELP Camera
Framerate: 120 fps
Latency: 60 ms
Price: $80
Connection: USB 2.0
Global Shutter
Notes: Abby
- OptiTrack was too expensive
- Pi had too high of a latency
- ELP was good middle ground
- global shutter good for capturing moving objects
- freeze frame pics w lil / no blur

## Slide 7: Major Components - Motors
NEMA 23 Stepper Motors | DM542T Stepper Drive
Specifications:
Steps / revolution
Current draw
Torque
Max voltage
Options:
NEMA 23 Stepper Motor
Brushless 3 Phase DC Motor
Synchronous Gear AC
Final Motor Choice: NEMA 23 Stepper Motor
1.8 steps/revolution
2.8A drawn per phase
1.9 Nm holding torque
48V max voltage
Final Motor Driver Choice: DM542T Stepper Driver
18 – 50 V DC Input voltage
1 – 4.5 A Output peak current
Multi-stepping for smooth motor movement
Notes: Abby
- stepper motor allows high accuracy, little speed/power sacrificed
- NEMA provides ample torque at good price
- DC would have provided high speed, but not enough accuracy
- AC motor are slower and lower torque

## Slide 8: Major Components – IR Sensors
Adafruit IR break beam sensors
Specifications:
Sensing distance
3.3V power voltage
Response time
Options:
Adafruit IR Break Beam Sensor
DFRobot IR Break Beam Sensor
Final Choice: Adafruit IR Break Beam Sensor
50 cm sensing distance
3.3V power voltage
10 mA current draw
< 2 ms response time
Notes: Abby
Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption

## Slide 9: Major Components – Scoreboard
74HC595 Shift Registers | 7-segment displays
Specifications:
Operating voltage
Low power consumption
Final Shift Register Choice: 74HC595
Availability
3.3V operating voltage
Low power consumption
Final Shift Register Choice: Common Cathode 7-Segments
Availability
Compatibility with Air Hockey Table
Notes: Abby
Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption

## Slide 10: Major Components – other
AMS1117 LDO
Specifications:
Output voltage
Output current
Options:
LMS1585ACS
Final Choice: AMS1117 Voltage Regulator
5V to 3.3V application
1A output current
Packaging
Industry standard
Notes: Abby
- does the right application, availability, convenience
Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption

## Slide 11: Major Components – other
Other major components
Limit switches for a secure gantry system
PC for handling all data received from the camera
Notes: Abby
- does the right application, availability, convenience
Choose the major (electrical) components being utilized by your design. For each component, provide a brief description of what it is, relevant specifications, and what it will do. Examples of major components include the microcontroller, motors, wireless interfaces, power converters and regulators. Examples of relevant specifications include operating speed (uC), number of I/O (uC), stall current (motors), operating voltage, and expected current consumption

## Slide 12: Block Diagram
Block Diagram
Notes: john

## Slide 13: Packaging Design
PCB housing
3D printed mount + lid
Notes: Pcb is 2.5 in x 2.35 in
Mounting holes r .116 in from each corner

## Slide 14: Packaging Design
PC housing
Where is the pc going
Wood Support for PC. Any laptop will fit on here.
Notes: Pcb is 2.5 in x 2.35 in
Mounting holes r .116 in from each corner

## Slide 15: Packaging Design
Power Supply Housing
Notes: Pcb is 2.5 in x 2.35 in
Mounting holes r .116 in from each corner

## Slide 16: Packaging Design
Power Supply Housing
Sensor Layout on underside
Notes: Pcb is 2.5 in x 2.35 in
Mounting holes r .116 in from each corner

## Slide 17: Packaging Design
Power Supply Housing
Notes: Pcb is 2.5 in x 2.35 in
Mounting holes r .116 in from each corner

## Slide 18: Packaging Design
Table Layout
Notes: John Include one or more images of your packaging design here. Include relevant dimensions and how you are planning to manufacture your product packaging.

## Slide 19: Packaging Design
This is the housing bracket for the motors. They will be manufactured using resin from a 3d printer.
Motor Bracket Housing
Notes: john

## Slide 20: Packaging Design
3D printed using PLA Filament
HUD Extension
Notes: john

## Slide 21: Packaging Design
Temporary design for Puck retrieval system.
Puck Retrieval System
Notes: john

## Slide 22: Electrical Schematic
Power
Notes: cameron
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 23: Electrical Schematic
Clock, micro, mounting holes
Notes: cameron
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 24: Electrical Schematic
Reset switch, programming header,
Notes: cameron
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 25: Electrical Schematic
spi
Notes: cameron
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 26: Electrical Schematic
Usb to uart ic
Notes: cameron
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 27: Electrical Schematic
3.3 to 5V Level Translator
Notes: cameron
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 28: Electrical Schematic
Gantry limit switch gpio
Notes: john
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 29: Electrical Schematic
Ir sensor gpio
Notes: john
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 30: Electrical Schematic
SPI to 7-segment
Notes: john
Include one or more views of your electrical schematic here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your schematics should be complete, organized, and readable.

## Slide 31: PCB Layout
Overview
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 32: PCB Layout
Power System with 5V Barrel Jack transformed to 3.3V for the rest of the board.
3.3V 5V
Power
Notes: cameron

## Slide 33: PCB Layout
Decoupling capacitors run on the underside of the board.
MicroController and Decoupling Capacitors
Notes: cameron

## Slide 34: PCB Layout
Programming header And reset switch
Notes: cameron

## Slide 35: PCB Layout
USB Mini-B Connector through USB<-->UART translator
USB Connector
Notes: cameron

## Slide 36: PCB Layout
LIMIT switches
Notes: cameron

## Slide 37: PCB Layout
Break Sensor Signals JOHN
Notes: cameron

## Slide 38: PCB Layout
Motor Control Signals
Notes: cameron

## Slide 39: PCB Layout
SPI
Notes: cameron

## Slide 40: PCB Layout
Oscillator and BOOT0
BOOT0
Crystal Oscillator
Notes: cameron

## Slide 41: PCB Layout
SPI overview
Notes: Include one or more views of your PCB Layout here. If necessary, break up this section into multiple slides detailing various subsystems which are easily viewable (Hint: a zoomed out view of a large electrical schematic in which nothing can be read will not be helpful for the design review). Your layout should be complete, organized, and readable.

## Slide 42: Prototyping Progress
Micro receives data over UART
Camera provides sufficient data to PC
PC identifies projected coordinates of a puck in motion
Micro turns the motors using the motor driver as expected
Micro interfaces with IR sensors to detect goals
Shift registers tested/verified with Arduino
Scoreboard tested and verified with Arduino
LDO has not yet been tested
Testing and verifying major components
Microcontroller
Motors
Motor Drivers
IR Sensors
Shift Registers
Scoreboard
LDO
Camera + PC
Component
Tested
Working
Notes
Notes: Abby
Describe your team’s prototyping progress here. For each of your project’s major components, what has been tested? What is known to work? What still needs to be tested, and what still needs to be proven to work?

## Slide 43: Prototyping Progress
Micro receives data over UART
Camera provides sufficient data to PC
PC identifies projected coordinates of a puck in motion
Micro turns the motors using the motor driver as expected
Micro interfaces with IR sensors to detect goals
Shift registers tested/verified with Arduino
Scoreboard tested and verified with Arduino
LDO has not yet been tested
Testing and verifying major components
Microcontroller
Motors
Motor Drivers
IR Sensors
Shift Registers
Scoreboard
LDO
Camera + PC
Component
Tested
Working
Notes
Notes: Abby
Describe your team’s prototyping progress here. For each of your project’s major components, what has been tested? What is known to work? What still needs to be tested, and what still needs to be proven to work?

## Slide 44: Prototyping Progress
Micro receives data over UART
Camera provides sufficient data to PC
PC identifies projected coordinates of a puck in motion
Micro turns the motors using the motor driver as expected
Micro interfaces with IR sensors to detect goals
Shift registers tested/verified with Arduino
Scoreboard tested and verified with Arduino
LDO has not yet been tested
Testing and verifying major components
Microcontroller
Motors
Motor Drivers
IR Sensors
Shift Registers
Scoreboard
LDO
Camera + PC
Component
Tested
Working
Notes
Notes: Abby
Describe your team’s prototyping progress here. For each of your project’s major components, what has been tested? What is known to work? What still needs to be tested, and what still needs to be proven to work?

## Slide 45: Prototyping Progress
Micro receives data over UART
Camera provides sufficient data to PC
PC identifies projected coordinates of a puck in motion
Micro turns the motors using the motor driver as expected
Micro interfaces with IR sensors to detect goals
Shift registers tested/verified with Arduino
Scoreboard tested and verified with Arduino
LDO has not yet been tested
Testing and verifying major components
Microcontroller
Motors
Motor Drivers
IR Sensors
Shift Registers
Scoreboard
LDO
Camera + PC
Component
Tested
Working
Notes
Notes: Abby
Describe your team’s prototyping progress here. For each of your project’s major components, what has been tested? What is known to work? What still needs to be tested, and what still needs to be proven to work?

## Slide 46: Prototyping progress
PSDR #1 (Hardware): An ability to use a microcontroller to control the XY directions of a gantry system using PWM and 2 motors.
PSDR #2 (Hardware): An ability to interface with an IC to establish communication and send data between a microcontroller and a PC via UART.
PSDR #3 (Hardware): An ability to interface a seven-segment display scoreboard with shift registers.
PSDR #4 (Hardware): An ability to keep score with a microcontroller by counting the number of times an interrupt is triggered by a puck passing through an infrared laser beam.
PSDR #5 (Software): An ability to estimate the position and trajectory of a puck in motion using computer vision.
Fulfilling psdrs
Notes: abby

## Slide 47: Prototyping Progress
Mechanical prototyping
Goals modified to support smooth image processing
Motor mounts 3D printed to fit into the side of the table
Side rails recently arrived, prototyping in progress
Notes: Abby
Describe your team’s prototyping progress here. For each of your project’s major components, what has been tested? What is known to work? What still needs to be tested, and what still needs to be proven to work?

## Slide 48: Mechanical prototyping
Gantry System
Notes: cameron

## Slide 49: Software Development Status
PC Components
Notes: joey

## Slide 50: Software Development Status
Microcontroller components
Notes: joey

## Slide 51: Software Development Status
Puck tracking on Pre-recorded video
Notes: joey

## Slide 52: Software Development Status
Puck tracking on Live video
Notes: joey

## Slide 53: Project Timeline
Gantt Chart
Notes: joey

## Slide 54: 3D Printing
Questions?